## Slide 1
Eliott Peron
09/09/2026
École d'Été Temps Réel - 2026
Embedded software In space

## Slide 2: Summary
IMA and TSP
Autocode
Space-ificties
01
To infinity and beyond
Validation
Quality
02
03
04
05
06

## Slide 3
Space-ificties
This document is the property of CNES. It cannot be used without their consent

## Slide 4: On-board: the spacecraft
01 - Space-ificties
Notes: PF :
  enjeux
  équipements
  scao
  télécoms
  évocation robustesse aux radiations
  haute criticité
CU :
  enjeux
  types d'instruments
  algorithmie bord
  missions & applications
  moindre criticité

## Slide 5: On-board: the spacecraft
  Specific on-board .
  algorithms .
Tele-
communication
  Specific operability
Specific instruments
(cameras, spectrometers, etc.) )
Radiations tolerance /
resistance
Thermal regulation
AOCS: Attitude &
Orbit Control System
01 - Space-ificties
PAYLOAD
PLATEFORM
Infrastructure enabling the mission High criticality
Spacecraft mission lower criticality
Notes: PF :
  Specific equiments & algorithms
  AOCS
  Telecoms
  Thermal regulation
  Resistance aux Radiations
  Enjeu : tout e qu’il faut pour faire permettra au satellite d’accomplir sa mission : haute criticité
CU :
  enjeux
  types d'instruments
  algorithmie bord
  missions & applications
  moindre criticité

## Slide 6: OBC: ON-BOARD COMPUTER
Spacecraft
01 - Space-ificties
OBC
FPGA matrix
Memories (RAM, QSPI, etc.)
Processor cores (CPU)
FSW
HW interfaces
HW interfaces
HW interfaces
Platform equipments
Payload instruments
Notes: OBC 1 ou plusieurs par mission on peut en avoir 1 pour la PF et 1 pour la CU voir plusieurs pour une CU complexe
C'est quoi / où : un composant électronique intégré sur le satellite (comparable processeur de PC)
il y a quoi dedans (des interfaces / des mémoires / un processeur / du FPGA)
Soit un FPGA couplé avec un processeur
Soit soc
Les types d’interfaces courantes : de l’i2c, du spi, du spw, de l’ethernet, de l’uart
Un peu ce que l’on veut grâce au FPGA

## Slide 7: A Quick history of On-board computers (1/3)
01 - Space-ificties
IMS T805E
STM: 32 bits transputer ; 2.2 MIPS* / 20 MHz
DEMETER, MYRIADE
2004
LEON3FT, GR712RC
Gaisler: 32 bits ; 80 MIPS* / 100 MHz ; SPARC V8 ; 2 cores
SCOC3 (SPOT 6)
2010
LEON5
NOEL5
RISC-V
NG-Ultra (NX) VERSAL (Xilinx)
FUTURE SPACE MISSIONS
2025+
ERC32
Temic Atmel: 32 bits ; 20 MIPS* / 25 MHz ; SPARC V7
PLEIADES
2001
LEON2FT
Atmel: 32 bits ; 80 MIPS* / 100 MHz ; SPARC V8
MEGHA-TROPIQUE
2008
LEON4, GR740
Gaisler: > 400 MHz, 4 cores
ZYNQ (Xilinx): > 600MHz, mass production
IDEFIX© rover, Nanosats, ATHENA
2019
*MIPS : Million Instructions per Second
Notes: Bref panorama de ce qui se faisait / se fait / se fera → intro vers cours 3 (HW)

## Slide 8: A Quick history of On-board computers
01 - Space-ificties
Xilinx Zynq-7xxx
2 ARM Cortex A9 cores
@ 400-800 MHz
(1000-2000 MIPS)
Xilinx UltraScale+
2 ARM Cortex R5 cores
@1GHz
4 ARM Cortex A53 cores
@500MHz
Xilinx Versal
2 ARM Cortex R5 cores
@1GHz
2 ARM Cortex A72 cores
@2GHz
IA engines
Microchip SAM3X
Cortex M3
@ 84 MHz
For equipments
Focus on COTS processors (Rad-Tol)
Notes: Bref panorama de ce qui se faisait / se fait / se fera → intro vers cours 3 (HW)

## Slide 9: A Quick history of On-board computers
Chart: 
| F9450 | MA3-1750 | MA3-1750 | T805 | ERC32 | LEON3 | GR712 (2 cores)
Main European Microprocessors in Space | 2 | 2 | 2 | 5 | 10 | 60 | 190
Spot4
Spot5
Proteus
Myriade
Pleiades
Spot6-7
Main European Microprocessors in Space (Rad-Hard)
MIPS*
Payloads /
equipments
Chart: 
| GR712 (2 cores) | Quadricoeur ARM Cortex-A7 | Intel Core i7 5960x
Main European Microprocessors in Space | 3000 | 30000 | 220000
In the meantime on PC…
MIPS*
Raspberry Pi 2
Desktop PC
01 - Space-ificties
Computers diversity and characteristics:
another source of complexity
Explosion of computing power
Resources limitations
Power
Weight
Space environment
Radiations
Particles
*MIPS : Million Instructions per Second
GR712 (2 cores)
Notes: Bref panorama de ce qui se faisait / se fait / se fera → intro vers cours 3 (HW)
Un processeur type i7 est 200 fois plus puissant qu’un proc d’un satellite traditionnel

## Slide 10: Which OBC for which mission?
01 - Space-ificties
      Deep space exploration, telecomunication or long-term missions, etc.
         Qualified OBC (LEON for instance)
NEED OF HIGH TRL
Earth observation or Science missions, heavy on-board treatments, etc.
    Future generation of qualified OBC (LEON for instance)
    Powerful COTS
NEED OF COMPUTING POWER
      New space or short terms missions, etc.
        Simple COTS
COST / AVAILABILITY CONSTRAINTS
  Depends on mission’s orbital characteristics
    Mostly qualified OBC
    Or COTS with extra test campaigns
HIGH RADIATIONS / VIBRATIONS / TEMPERATURE TOLERANCE
      Mechanical, thermal, power consumption constraints, centralized of decentralized spacecraft…
        One or several OBC, with one or several processor cores each.
ARCHITECTURE CONSTRAINTS

## Slide 11: Focus on space envrionment
01 - Space-ificities
This document is the property of CNES. It cannot be used without their consent
EXTREME TEMPERATURES
+200°C in the light
-273°C in the shadow
 Constraints on spacecrafts architecture and functionnalities
ROUGH RADIATIVE ENVIRONMENT
Ionizing particles
Leading to electronics malfunction (SEU, SEL, etc.)
 Constraints on spacecrafts architecture, ability to communicate, and fucntionnalities
RISK OF DEBRIS
Atmosphere is thin, but still there  friction
Collision with debris detection and avoidance
 Constraints on spacecrafts architecture, maneuverability
Notes: Les laisser proposer des solutions pour mitiguer les SEU

## Slide 12: Component selection : radiation
01 - Space-ificities
Latchup : “ high current flows and if the power supply is maintained, the device can be destroyed by thermal effect.”
SEU “An SEU is a single bit flip, i.e. the change of state of a storage element, such as flip-flops, latches or SRAM cells”
TID ” Induced by the transfer of ionising energy from the radiation exposure, which thermalized in the creation of electron-hole pairs in the component material. “
Galactic cosmic rays deposit energy in an electronic device, after Lauriente and Vampola).pdf
This document is the property of CNES. It cannot be used without their consent

## Slide 13: Component selection : radiation
  RadHard (Radiation Hardened)
    built for radiation (specific silicon process/PDK or IP library)
    Radiation guaranteed by datasheet
    Space quality certified ESCC or QML
    silicon die controlled tracability
  COTS (Commercial Off-The-Shelf)
    Generic application component (built for other market than space)
  RadTol (Radiation Tolerant)
    « everyday component » sold for space use
    most of the time COTS rebranded for space after dedicated tests
    radiation data and qualification variable
+ | +++ | +++
++ | ++ | ++
+++ | + | +
  Performance
  Price
  quality
  RadHard
  RadTol
  COTS
01 - Space-ificities
This document is the property of CNES. It cannot be used without their consent
Notes:   Composant RadHard (Radiation Hardenned)
    Conçu pour les radiations ( Techno ou bibliothèque spécifique)
    Données radiation « contractuelles » (mesures faites par le fabriquant)
    Souvent qualifié selon une norme ESCC ou QML
    traçabilité de la puce garantie
  Composant RadTolerant :
    Argument commercial du fabriquant (surveiller les données) . souvent des composants commerciaux testés et « re-brandés » par le fabriquant
    souvent la dose est mise en avant (attention la dose spatiale est lente différent de la dose pour certaines applications )
    pas de qualification
    données radiations non fournies
    fabrication non garantie reproductible (usine différente, changement de masque de fabrication) => impact sur les données radiations

## Slide 14: Component selection : thermal
Temperature range (ex. from -157°C to +121°C (ISS profile)
  Consider using extended temperature range
Gradient and dissipation
  take care of the board component place
01 - Space-ificities
This document is the property of CNES. It cannot be used without their consent

## Slide 15: Component selection : Mechanical
Impact:
  Component pitch and size
  Component material
  Component position on board
ST 65nm space
SMX5 board
01 - Space-ificities
This document is the property of CNES. It cannot be used without their consent

## Slide 16: Missions of Flight Software
01 - Space-ificities
Boot/automatic seq.
Modes
Time
Monitoring
Memories
MANAGEMENT
AOCS
Thermal / Power control
Navigation
Payload algorithms
PROCESSING
TM/TC
On-board protocols
(inter-sat protocols)
COMMUNICATION
ON-BOARD SOFTWARE ACTIVITIES
AMOUNT OF REAL-TIME FUNCTIONS: A SOURCE OF COMPLEXITY
Several real-time cycles
Asynchronous treatments
Several priorities
Hard-real-time constraints (equipments, fault detection)
Notes: Les missions, en gros (s'assurer qu'il démarre bien / lien IF / s'assurer de la bonne santé du sat / l'algorithmie bord / l'autonomie du sat / la communication avec le sol / la gestion des données et des versions du sat)

## Slide 17: Focus on software embedded within equipment
01 - Space-ificities
(incomplete) LIST OF EQUIPMENT CONCERNED
THE SOFTWARE INSIDE
WHAT ABOUT CRITICALITY?
Reaction Wheels
Thrusters
SADM
(Solar Array Drive Mechanism)
Cameras
Very small
(~5000 lines of code maximum)
Mostly runs on µcontrollers
Equipment turn ON/ OFF
Execute output orders (ex: turn solar array)
Send data (ex: camera image)
Main functionnalities
Depends on equipment’s usage
Payload instrument or software reloadable:
Less critical
Platform equipement:
Critical
Software Development & Quality
Often developed by equipemnt architects
… who are not software experts
The level of quality has to be controlled
Notes: Une (légère) digression : le LV des équipements spatiaux
De quels équipmeents parle t’on ? Roues de réactions, startrackers, SADM, cameras
Quelle taille de logiciel : tout petit, tourne sur des microcontrôleurs, qu’estc-e que ça fait ? ON / OFF, pilote par rapport à une consigne, envoie de données
Quels besoin de criticité: ça dépend
En pratique coment c’est fait : sur un con de table par des gnes sont c’est pas trop le métier… y a des vrais challenges – anecdote

## Slide 18: Constraints for Flight software Everyday constraints
AMOUNT OF REAL-TIME FUNCTIONS
COMPUTERS DIVERSITY AND CHARACTERISTICS
Type and number of available memories
Number of OBCs to manage
CPU frequency and number
Maturity (TRL) and
resistance of OBC
Storage size of FSW: binaries files
Execution space for FSW: RAM size
Communication between embedded functions
Execution time and frequency of embedded functions
Quality level of embedded functions
01 - Space-ificities
Notes: Les contraintes : empreinte mémoire, empreinte temporelle / grande variété d'applications qui doivent s'exécuter en parallèle

## Slide 19
IMA and TSP
This document is the property of CNES. It cannot be used without their consent
Notes: Poser la question et les laisser répondre.
Le résultat d’un système temps-réel doit être correct dans l’intervalle de temps où la réponse est attendue  On parle de « Deadline »
Sinon il est incorrect.
On entend parler parfois de deux type de temps-réel:
Soft : un deadline miss résulte uniquement en une baisse de la qualité de service du système. Trouver un exemple
Hard : un deadline miss résulte dans une erreur critique du système.

## Slide 20: IMA An inspiration from aeronautics
9 functions, 9 computers.
9 functions, 2 identical computers.
IntegratED modular avionics Concept developed for aircrafts and widely deployed on Airbus and Boeing spacecrafts since A380 and B777.
02 – IMA and tsp
      Basics Principles :
        Capture the needs (in CPU power and I/O) from all the functions of the aircraft
        Select the appropriate number of computers and switches allowing to cover all the needs
        Distribute all the functions across the computers
        Configure the network
This document is the property of CNES. It cannot be used without their consent

## Slide 21: IMA building blocks
But IMA could be possible only thanks to strong design properties:
A deterministic and configurable network (AFDX)
An on-board software architecture allowing to guarantee:
  Strong segregation between applications hosted by the same computer (confinment of anomalies during software execution)
  An independant development and validation between the different hosted applications (potentially qualified by different suppliers)
An architect / integrator in charge of managing all the rationalization:
  Capture the needs (in CPU power and I/O) from all the functions of the aircraft
  Select the appropriate number of computers and switches allowing to cover all the needs
  Configure the distribution of all the functions across the computers
  Configure the network
02 – IMA and tsp
This document is the property of CNES. It cannot be used without their consent

## Slide 22: IMA benefits
Benefits:
Reduction of the number of HW to qualify (+ SW execution platform)
Very fast reliability of the HW (+ SW execution platform) used (intensively used in many different ways by different suppliers).
Capability to decrease the quality assurance level of software applications that have a lower criticality rather than always apply to all of them the worst criticality of the computer.
Capability to host several SW functions, potentially from different suppliers on the same processor/SoC, while keeping an independent qualification process between these functions.
Reduction of weight, volume and consumption of electronics
This on-board software architecture has been described in the ARINC653 standard and relies on Time and Space Partitioning.
Drawbacks:
A single component is used in many computers : common failure mode.
Suppliers loose their skills in HW developments and SW execution platform
02 – IMA and tsp
This document is the property of CNES. It cannot be used without their consent

## Slide 23: What is Time and Space PArtitioning ?
Static memory allocation
Static time allocation
= no dynamic preemption
XNG
P1
P2
P3
P4
XNG
Memory space
CPU time
0
T
P5
Concept
Each application software is called a partition and has its own memory space and time slots allocated on the CPU.
This segregation of resources makes possible to develop and qualify each application independently.
XNG
CPU#0
T
CPU time
CPU#1
T
02 – IMA and tsp
This document is the property of CNES. It cannot be used without their consent

## Slide 24: TSP : advantages and drawbacks
  Advantages
      Allows an independent development and validation of the different partitions (absence of non functional side effects).
      Ease the reuse of recurrent functions.
      Ease the performances analysis (WCET and reactivity) because much less preemptions by other functions (and less functions per software).
      Capability to decrease the quality assurance level of software applications that have a lower criticality rather than always apply to all of them the worst criticality of the computer.
  Drawbacks
      CPU and memory overhead (but acceptable for space OBSW projects)
      The CPU time that is not consumed by one partition can not be used by the others.
      Incompatible with strong response time ( < 10ms) required by HW.
  Crucial role of the resource allocation to guarantee the coverage of Project requirements without impacting the qualification context of the other partitions.
02 – IMA and tsp
This document is the property of CNES. It cannot be used without their consent

## Slide 25: Sharing I/O devices across partitions
FPGA/SoC IP
P1
P2
P3
I/O link
SW
HW
HW registers
Ctrl/status
I/O server
Mandatory to have a server component for shared devices to guarantee an independent QoS (Quality of Service) for client partitions, that is the corner stone of IMA/TSP
02 – IMA and tsp
This document is the property of CNES. It cannot be used without their consent

## Slide 26: CPU budget for such an I/O server component
TSP : no immediate reactivity with interrupts ! Polling becomes much obvious.
=> The only crucial question is : what is the worst acceptable response time ?
Schedule the IO partition according to the needs of each client partition wrt :
Throughput
Latency
Periods
But also :
Duration of each emission/reception
Level of HW support for these operations (byte-per-byte, complete message, n messages, virtual channels, …)
02 – IMA and tsp
This document is the property of CNES. It cannot be used without their consent

## Slide 27: CPU budget for such an I/O server component
02 – IMA and tsp

## Slide 28: KOSMOS
28
Our goal
Provide our ecosystem with a generic software infrastructure that standardizes essential functions and allows users (eg. Scientists) to focus solely on the added value of the space mission.
»
»
CCSW
HSEM
IOS
MMDL
NAV
AOCS
Hyperviseur (XtratuM-NG)
µP
…
Payload 2
Payload1
A653
Components available off-the-shelves #DevOps
All the components are qualified ECSS-B.
Risks reduction thanks to a modular and mature infrastructure
FASTER
BETTER
CHEAPER
02 – IMA and tsp

## Slide 29
Autocode
This document is the property of CNES. It cannot be used without their consent

## Slide 30: AUTOCODING AT CNES: an origin story
03 - Autocode
~2010
DEMETER
AOCS algorithm prototype
End-of life experiment
2010
PICARD
AOCS algorithm prototype
End-of life experiment
2016
MICROSCOPE
Several AOCS modes
No equipment-specific
functionalities
2024
MICROCARB
Several AOCS modes
No equipment-specific
functionalities
Very specific use-cases
Manual integration within complex Flight SoftWares
Huge validation effort
No ECSS compliance
No format coherency between autocodes
This document is the property of CNES. It cannot be used without their consent
Notes: At first these activities had a huge impact on software development teams, who had to manually integrate autocodes within complex FSW, with strong adherence between AOCS algorithms and equipment drivers. The validation effort was substantial (all unitary testing was made by hand directly on generated code), which led to heavy additional testing activities whenever an autocode modification/bugfix was necessary.
Generated code was not ECSS-compliant, and there was no format coherency between autocodes.

## Slide 31: AUTOCODING AT CNES: an origin story
03 - Autocode
2019
EYESAT
Full AOCS
2023
NESS
Full AOCS
2026
IDÉFIX (MMX) Rover
Full ACS
NEW SPACE: A CHANGE OF PARADIGM
Increase of onboard computing power
Lower budgets
Strong time constraints
Increasing complexity of onboard treatments
Increasing diversity of use-cases
Startracker
algorithms
Image Detection
algorithms
RF
algorithms
Emergence and consolidation of an "autocoding process" at CNES
This document is the property of CNES. It cannot be used without their consent
Notes: Historically code generation was used to help AOCS algorithms development and integration, but in the last few years, with the increase of onboard computing power and the emergence of strongly time-and-budget-constrained New Space projects (EyeSat, N3SS, MMX Rover), its scope became wider and wider.

## Slide 32: From concept…
03 - Autocode
Matlab®
Simulink®
Coding Rules
Readability
Consistency
Code generation compatibility
AOCS algorithm model
Safe Mode
Model
Nominal – Guidance 2 Model
Nominal – Guidance 1 Model
Nominal – Guidance 3 Model
Matlab functions
Sensors Models
Actuators Models
Environment Models
Complete Simulator
Validation Scenarios (MIL)
Tuning simulation campaigns
Performance simulation campaigns
Robustness simulation campaigns
This document is the property of CNES. It cannot be used without their consent
Notes: ultimately, a simulator. This simulator consists of models representing the algorithm to be implemented in the FSW and models of the environment and equipment.
Once the simulator is assembled, tuning simulation campaigns, as well as performance and robustness simulation campaigns are performed in Model-In-the-Loop (MIL) mode, to validate and verify the developed software.

## Slide 33: … To autocoded algorithm
Embedded Coder
03 - Autocode
AOCS algorithm model
SAFE
Model
Nominal – Guidance 2 Model
Nominal – Guidance 1 Model
Nominal – Guidance 3 Model
Matlab functions
Embedded Coder
Configuration
Machine learning qualification Handbook
ECSS-E-HB-40-02A
MathWorks recommendations
Simulink Notes & Report generator
AOCS Autocode Package
This document is the property of CNES. It cannot be used without their consent
Notes: June 2021 : handbook describing the process of generating code from models and guidelines related to this process.
Embedded Coder allows significant time, human and financial resources savings to produce on-board applications. This approach eliminates the need to recode, in another language, algorithms that were developed for simulation and tuning purposes in MATLAB/Simulink.
Simulink Notes: comment his/her Simulink code at the same time he/she develops it. These notes can be exported to a word document with the report generator toolbox, allowing an automated generation of the model description document.
configuration of Embedded Coder has been selected carefully and is a trade-off between the configuration recommended by Mathworks and the configuration recommended by the ESA Handbook. The configuration depends on the MATLAB/Simulink version, and thus is updated when necessary.
After these steps are completed, the process of generating code can be started using the appropriate toolboxes. Prior to code generation, an internal tool checks compliance with the coding rules. Then, if compliant, code is generated in a ready-to-use delivery package.

## Slide 34: autocode package
03 - Autocode
Autocode (.c/.h)
Autocode API:
  AOCS_autocode_initialize()
  AOCS_autocode_step()
Refruns (reference tests)
Inputs
Parameters
Expected outputs
Model validation reports
Matlab / Simulink sources
Autocode package configuration / traceability
This document is the property of CNES. It cannot be used without their consent

## Slide 35: Autocode integration
Main loop (while(1))
03 - Autocode
AOCS Autocodes Execution
Environment Setup
Call AOCS_autocode_initialize();
Read partition inputs (through ports / buffers)
Fill autocode input structure with (formatted) partition inputs
Call AOCS_autocode_step();
Convert autocode output structure content into (formatted) partition outputs
Write partition outputs (through ports / bufers)
Setup AOCS parameters with default values
Refrun parameters
This document is the property of CNES. It cannot be used without their consent

## Slide 36: Partition validation facility
03 - Autocode
Resident Software (RSW)
partition-level test FSW
PARTITION
under test
Hypervisor (XtratuM-NG)
OUT
OUT
TRACES
OUT
IN
SANDBOX partition
Sandbox Test scripts
OUT
TRACES
IN
IN
IN
UART / Memory Dump Logs
(including Sandbox instrumentation traces)
Test reports
Tests Logs Checker
This document is the property of CNES. It cannot be used without their consent

## Slide 37
Validation
This document is the property of CNES. It cannot be used without their consent
Notes: May not be real-time
A washing machine is an embedded system.
A flight SW runs on an embedded system and most applications have real-time needs

## Slide 38: WHY TO USE A SIMULATOR ?
04 - validation
« A simulator is a technical device (software or/and hardware) to reproduce at a chosen or possible level the behavior of a real phenomenon or a physical or functional system. »
This document is the property of CNES. It cannot be used without their consent

## Slide 39: Why not the real system ?
04 - validation
Availability
  Not yet built
  Not available for testing
Costs
Complexity
  Not easily configurable
  Need to parallelize
  Closed loop needs
  anomalies
Security
  Risk of damage
This document is the property of CNES. It cannot be used without their consent

## Slide 40: EXAMPLE : satellite simulator
04 - validation
Satellite
In orbit
Ground network
Remote control
Telemetry
Test Mgnt through GUI
Remote control
Telemetry
TOMS Training Operations and Maintenance Simulators
Station model
Ground segment
This document is the property of CNES. It cannot be used without their consent

## Slide 41: WHICH KINDS OF SIMULATORS for which goals ?
04 - validation
Studies
O
A
B
C
D
E
F
Study simulators
Performances analysis
Technical solutions/Algorithms
New concepts analysis
Tuning
Simulators by theme
AOCS validation
Thermal/Electrical validation
Flight software validation
Sub-system functional chains validation
System simulators
System functional chains validation
Technical Qualification
Operational Qualification
Future operators training
Investigations in case of anomalies
AIT simulators
This document is the property of CNES. It cannot be used without their consent

## Slide 42: SimulatOR OVERVIEW
04 - validation
Model library
Simulator =  of models
DEVELOPING

Variante =  of instances
(instance = configurated model)
CONFIGURING

Test driver
Driving the simulation
RUNNING
Scenario

ANALYSING

A model
is a basic building block of the simulator, which simulates a feature or piece of equipment, configured and connected to each other
This document is the property of CNES. It cannot be used without their consent

## Slide 43: Main KindS of simulators/Test benches
Processor in the loop (PIL)
Fully numerical
Hardware in the Loop (HWIL)
04 - validation
This document is the property of CNES. It cannot be used without their consent

## Slide 44: Sensors/Actuators models or other equipments
04 - Validation
Separation of (all of which being optionnal)
Functionnal simulation => Physics, measurements. Either modeled by a simple function or by using more complex libraries.
Command-Control simulation
Protocol simulation
Example of models :
Antennas : X-band, S-band, Inter-Satellite Link
Sensors : Sun Sensors, Magnetometers, Star Trackers, GNSS
Actuators : Reaction Wheels, Thruster, Magnetotorquers
Electrical Power : Battery, Solar Array, PCDU
Payloads
This document is the property of CNES. It cannot be used without their consent

## Slide 45
Quality
This document is the property of CNES. It cannot be used without their consent

## Slide 46: ecss
05 - QUality
3 types of documents
  Standard – « ST » Applicable requirements
  Handbook – « HB » Guides / Recommandations for applying applicable requirements
  Technical Memorandum – « TM » In the process of standardization
4 branchs
  Management « M »
  Engineering « E »
  Quality « Q »
  Sustainnability « S »
https://ecss.nl/
This document is the property of CNES. It cannot be used without their consent
Notes: ECSS standard européen :
Définit un ensemble de règles pour le développement d’un projet spatial
À différent niveau : des documents à livrer à des règles d’implémentation.
Exemple BR
Exemple empreinte mémoire

## Slide 47: Applicable standards
05 - QUality
Q-80 & E-40 applicable requirements are implemented according to SOFTWARE CRITICALITY
ECSS-S-ST-00C
SYSTEM DESCRIPTION
SPACE PROJECT MANAGEMENT BRANCH
M40
CONFIGURATION ET INFORMATION MANAGEMENT
SPACE PRODUCT ASSURANCE BRANCH
Q30
DEPENDABILITY
Q40
SAFETY
Q80
SOFTWARE PRODUCT ASSURANCE
SPACE INGENEERING BRANCH
E40
SOFTWARE ENGENEERING
This document is the property of CNES. It cannot be used without their consent
Notes: For SW, there are 2 ECSS standards that are applicable according the SW criticality :
ECSS-Q-ST-80 for SW Product Assurance
ECSS-E-ST-40 for SW Engineering
There are also the M40 for the configuration management, including SW
And the Q30 for dependability and Q40 for safety, especially to define the criticality

## Slide 48: Functional criticality
05 - quality
Remarkable differences between criticality classes
  Usually for C : decision coverage unmeasured / statement coverage = 100%
  Usually for D : decision coverage unmeasured / statement coverage = 80%
This document is the property of CNES. It cannot be used without their consent
Notes: The main differences between SW criticality classes are as follows
ISVV (Independant Sw Validation and Verification) is only required for SW criticality A and B
ISVV requires that the tester be different from the developer.
For criticality A, the company must be different, wheras for criticality B, the company can be the same but the team must be different
Then, the level of the metrics differs according to criticality levels …
And also the code coverage differs :
usually, 100% decision coverage is required for criticality B
usually, 100% statement coverage is required for criticality C
usually, 80% statement coverage is required for criticality D

## Slide 49: Coding standards for C
05 - Quality
Misra C 2012
coding standard
(from automotive industry)
RNC
coding standard
(common + C + embedded)
KOSMOS
coding standard
(tailorization from RNC)
https://www.misra.org.uk/
RNC-CNES-Q-HB-80-501
RNC-CNES-Q-HB-80-536
LVCUGEN-SPAP-AQ-0271-CNES - LVCUGEN Coding Standard.pdf
  RELIABILITY, SECURITY & MAINTAINABILITY
This document is the property of CNES. It cannot be used without their consent
Notes: To verify the quality of code written in C language, there are some standards that define coding rules to ensure the RELIABILITY, SECURITY & MAINTAINABILITY of embedded SW
The most famous is the MISRA C standard, created for automative industry but also used to develop other embedded systems
There are also The CNES coding standard and the KOSMOS coding standard which is a tailoring of several standards and tools
The philosophy is to have 1 coding standard for each language and of course a tool to verify these coding rules

## Slide 50: Onboard software pipelines at CNES
05 - QUALITY
P1 : Quality pipeline to check C rules
P2 : TU/TI pipeline for tests at partitions level
P3 : TV pipeline with full software
P4 : Delivery pipelline
First with jenkins, now with gitlabci
This document is the property of CNES. It cannot be used without their consent

## Slide 51
To infinity and beyond
This document is the property of CNES. It cannot be used without their consent

## Slide 52: 02 - current trends Focus on 5 axes (non-exhaustive)
1 - On-board autonomy
2 - Software-defined & reconfigurable architectures
3 – Hardware targets (No HW…No SW !)
4 - Development & testing
5 - Modularity and updates
This document is the property of CNES. It cannot be used without their consent

## Slide 53
06 - Future
10/15 years ago
Rule‑based FDIR*
Almost all data processing done on ground
Autonomous navigation limited to deep‑space probes
02 - current trends [1/5] On-board autonomy
53
2026 +
On‑board inference (image triage, anomaly detection)
Autonomous navigation & advanced FDIR
This document is the property of CNES. It cannot be used without their consent

## Slide 54
02 - current trends [2/5] Software-defined & reconfigurable architectures
54
10/15 years ago
Hard‑wired payloads
Minimal reconfiguration capability
Minimal in‑orbit retasking capabilities
FPGA updates rare and highly constrained
2026 +
Fully reconfigurable navigation payload (e.g. Galileo 2nd Gen)
In‑orbit reprogrammable telecom platform (e.g. ESA Electra SDR )
NanoSats using Zynq7000 for adaptive mission logic
This document is the property of CNES. It cannot be used without their consent
06 - Future

## Slide 55: 02 - current trends [3/5] Targets & architectures
06 - future
55
10/15 years ago
Rad750 (2005‒2015) dominated deep-space missions
LEON2/LEON3 used extensively in ESA missions
Strict avoidance of COTS CPUs for LEO missions
2026 +
ARM-based COTS compute stack (OneWeb)
High-end smartphone-class SoCs in orbit (OPS-Sat / ESA)
Increasing adoption of RISC‑V (e.g., ETH Zürich deployments)
This document is the property of CNES. It cannot be used without their consent
Notes: Exemple de target cots utilisé pour des missions :
Sapdragon sur ingenuity

## Slide 56: 02 - current trends [4/5] Development & testing
06 - future
56
10/15 years ago
Paper/Word/PDF requirement workflows
Limited system‑model integration
Verification mostly manual and slow
2026 +
Increase of end‑to‑end MBSE workflows (e.g. ESA using Capella/Arcadia)
Increasing use of digital twins* (Juice, ExoMars rover, and Ariane 6 avionics…)
Automated regression pipelines for flight software (GitlabCI, Jenkins…)
*digital twins : real-time virtual replicas of physical objects, systems, and processes
This document is the property of CNES. It cannot be used without their consent
Notes: Expliquer ce qu’est un digital twin

## Slide 57: 02 - current trends [5/5] Modularity & updates
06 - future
57
10/15 years ago
Security was mostly a compliance checklist, not architectural
Very limited OTA update capability
Monolithic flight software with large restart penalties
2026 +
Secure boot and hardware root of trust in new ESA LEO missions
Partitioned OSes (e.g. RTEMS SMP, seL4 research payloads)
Starlink and OneWeb perform fleet‑wide OTA* updates
*OTA : Over The Air update
This document is the property of CNES. It cannot be used without their consent

## Slide 58: 02 - current trends How can we support these changes ?
06 - Future
58
On the HW side
Support new architectures (AI engines, RISC-V, GPU, dedicated IPs…)
Power consumption
Thermal dissipation
Radiation tolerance
On the SW side
Support new Operating Systems to enable new kinds of applications
Compliance with Space standards ? (e.g. ECSS)
Real time capacities ?
Memory footprint,
This document is the property of CNES. It cannot be used without their consent

## Slide 59: 02 - current trends How can we support these changes ?
06 - Future
59
On the SW side
Support new Operating Systems to enable new kinds of applications
Compliance with Space standards ? (e.g. ECSS)
Real time capacities ?
Memory footprint,
How can Linux helps flight software
move to the next step ?
-> Hardware trends are not detailed in the frame of this course
On the HW side
Support new architectures (AI engines, RISC-V, GPU, dedicated IPs…)
Power consumption
Thermal dissipation
Radiation tolerance
This document is the property of CNES. It cannot be used without their consent

## Slide 60: 03 - Focus on Linux : A brief history
06 - Future
60
Linux and embedded systems : a success story !
Late 90s : μClinux enabled ports to a large variety of microprocessors
2000 : Arm-Linux synergy : low costs, low power consumption, and low heat generation
2005 : PREEMPT_RT project was initiated to provide a patch to the Linux kernel (enable real time features)
2008 : Android 1.0 was released, based on the Linux kernel
2024 : Embedded Linux is used in 44%-46% of embedded systems "Embedded Systems Statistics By Market Size And Technologies". Electro IQ. 24 February 2025
Embedded Linux 2026 trends : Edge computing, IOT (on Earth… but also in Space !)
Image source : https://electroiq.com/stats/embedded-systems-statistics
This document is the property of CNES. It cannot be used without their consent
Notes: Preempt_rt un moyen de patcher le noyau linux afin de le rendre plus déterministe.
Depuis quelques années c’est maintenant de base dans le kernel linux

## Slide 61: 04 - Linux for space applications
06 - Future
61
Most applications coded in C language
Specific hardware
(radiation tolerant for example)
Specific software
(compliant to space standards)
Small community
Lack of support
Increasing complexity (both HW and SW)
Today

## Slide 62: 04 - Linux for space applications
06 - Future
62
This document is the property of CNES. It cannot be used without their consent
Most applications coded in C language
Specific hardware
(radiation tolerant for example)
Specific software
(compliant to space standards)
Small community
Lack of support
Increasing complexity (both HW and SW)
NEW
SPACE
Today

## Slide 63: 04 - Linux for space applications
06 - Future
63
This document is the property of CNES. It cannot be used without their consent
Most applications coded in C language
Specific hardware
(radiation tolerant for example)
Specific software
(compliant to space standards)
Small community
Lack of support
Increasing complexity (both HW and SW)
NEW
SPACE
Today

## Slide 64: 04 - Linux for space applications
06 - Future
64
Most applications coded in C language
Specific hardware
(radiation tolerant for example)
Specific software
(compliant to space standards)
Small community
Lack of support
Increasing complexity (both HW and SW)
NEW
SPACE
Allow the use of high level languages
Ease application porting
Plenty of compatible targets
Large community
Lot of support / documentation
Today
Tomorrow with Linux ?
A magic solution… really ?
Notes: Developpement d’app pour gain d’autonomie à bord plus facilement

## Slide 65: 04 - Linux for space applications
06 - Future
65
This document is the property of CNES. It cannot be used without their consent
Linux in Space is not that new…

## Slide 66: 04 - Linux for space applications
06 - Future
66
Flight Linux project [NASA] : extend COTS philosophy to software domain (kernel + APP : 500Ko, system RAM 4MB)
X-Sat [Nanyang Technological University] : Linux on several StrongArm SA1110 processors for a payload controller
Aalto-1 [Aalto University] : AT91RM9200-based Embedded computer, Linux 3.4 prepared with buildroot
2003
2005
2007
2011
2013
2015
2017
QuakeSat [QuakeFinder LLC] : PC/104 x86 CPU module with Red Hat Linux
UWE-1 [University of Würzburg] : Hitachi H8S 2674 16-bit with μClinux
MidSTAR-1 [United States Naval Academy] : ARM Linux on a payload controller
2010
Falcon 9, Dragon [Space X] : Multiple COTS computers, custom Linux 3,2 with real-time patches
IPEX [Cal Poly San Luis Obispo, JPL] : 400MHz Atmel ARM9, Linux 2.6.30
LightSail-1 [The Planetary Society] : Tyvak Intrepid v6 single-board computer
PhoneSat satellites [NASA] : Google Nexus One and Nexus S with Android 2.2
Dove satellites [Planet] : Low-power COTS x86 processors, Ubuntu server
2019
OPS-SAT [ESA] : Altera Cyclone V SoC (ARM dual-core Cortex-A9 MPCore, Cyclone V FPGA)
1999
Notes: À noter :
Space X sur leur lanceur falcon 9 sur leur capsule crew dragon sur starlink
Nasa avec ingenuity 2021 mars persévérance

## Slide 67: 04 - Linux for space applications
06 - Future
67
What do we fear ?

## Slide 68: 04 - Linux for space applications
06 - Future
68
  Real time constraints (memory, timers, scheduling…)
  Security (updates, unsafe languages, kernel complexity, ground/on-board communication…)
  Base level system requirements (kernel configuration, service management, system initialization, log system, file system…)
  Deployment / OTA updates
  Licence / export control
Notes: Base level requ : est-ce que le HW à ce qu’il faut pour supporter une image linux
Licence : pour un plateformiste qui voudrait un logiciel pour sa plateforme générique la question de la licence va se poser
Deployment /update : recharger une image linux qu’est ce que ça veut dire comment déployer un nouvel applicatif

## Slide 69: 05 – LINUX and KOSMOS
06 - Future
69
Embedding an application catalog
Switch to another application when the experience is done
Load new applications from ground
Delete on-board applications if they are not needed anymore
Nothing less than a smartphone in orbit !
Notes: Comme on l’a vu on cherche :
à avoir de plus en plus d’autonomie à bord
et le new space pousse pour des développements rapide

## Slide 70: 05 – LINUX and KOSMOS
06 - Future
70
No Space standard for embedded Linux yet (ongoing work – Space Grade Linux)
Container-based modular approach to ensure tasks segregation
Multi-politic scheduling approach to optimize CPU occupancy
Notes: SGL : groupe de travail afin d’établir les bonne pratiques sur l’utilisation de linux dans le spatial et la génération d’une image pour le spatial
mais on est encore aux prémices
Container : virtualisation de plusieurs environnements linux sur un même hote et basé sur le même kernel mais isolé

## Slide 71: 05 – LINUX and KOSMOS
06 - Future
71
How to build and tune Linux for our needs ? The Yocto project
An open source collaboration project that helps developers create custom Linux-based systems regardless of the hardware architecture.
Provides a flexible set of tools and a space where embedded developers worldwide can share technologies, software stacks, configurations, and best practices
Used to create tailored Linux images for embedded and IOT devices, or anywhere a customized Linux OS is needed.
Notes: Projet open source colaboratif de génération d’image linux pour l’embarquer ajuster au besoin

## Slide 72: 05 – LINUX and KOSMOS
06 - Future
72
How to build and tune Linux for our needs ? The Yocto project
Recipes : files that describe how to fetch, configure, build, and install a piece of software in an embedded Linux system.
Layers : Collection of files that describes a specific part of the future Linux distribution (= collection of layers)
Yocto : Set of tools used to generate the Linux distribution (boot + dtb + kernel + filesystem)
Filesystem
/usr
/home …
BOOT
Device Tree Blob (dtb)
Kernel

## Slide 73: 05 – LINUX and KOSMOS
73
Starts from poky (core-image-minimal)
Scarthgap branch
Use of PREEMPT-RT patch
Use of systemd for service management
Use of specific XNG (hypervisor) layer (Linux as guestOS + inter partitions communication)
Use of specific PUS layer
Only one payload application running on Linux
Yocto Poky
XNG
KOSMOS
App Store
PUS
SGL (Space Grade Linux)
Yocto layers for KOSMOS environment
Notes: Poky c’est l’image de base mise à dispo par yocto avec le minimum vital

## Slide 74: 06 - New use cases : AUTONOMY
06 - Future
74
SESAM example
SESAM : Space Experiment for Satellite Artificial intelligence Monitoring
AI application using models to detect anomalies in telemetry data produced by the satellite's various instruments.
Enables systematic and continuous monitoring of multiple parameters while limiting data exchange between the ground and the edge.
Autonomous decisions made by the on-board computer following an anomaly. (i.e. restarting a non-critical partition)

## Slide 75: 06 - New use cases : SWARMS & constellations
06 - Future
75
This document is the property of CNES. It cannot be used without their consent
SWARM : A group of satellites flying in close formation, exchanging data and performing computations that can be distributed.
Constellation: A group of identical satellites that work together to provide a service, generally ensuring almost complete coverage of the globe.

## Slide 76: 06 - New use cases : SWARMS & constellations
06 - Future
What challenges ?
Inter-satellites communication
Navigation control algorithms
Cyber security
Continous updates
Complexity related to distributed systems

## Slide 77: 06 - New use cases : Robotics
06 - Future
77
Space ROS with embedded Linux
What is ROS ?
Robot Operating System : set of software libraries and tools that help build robot applications
Why use ROS for Space applications ?
Reduce project costs and schedule (widely use on Earth !)
Integrate open source flight heritage apps
Transistion technology from desktop-to-flight
Space ROS for what ?
Martian/lunar robots
Operating arms
LORA (see illustration)

## Slide 78: TO REMEMBER
06 - future
New kinds of on-board proccessings need the flight software to adapt (AI, distributed computing, use of high-level languages…)
Linux can help move to the next step but is not a magic solution !
  Lack of garuantees regarding space standards
  No strong real-time guarantees
  Not ready for critical processings yet (typically platform processings)
  Easily usable for non-critical applications (typically payload processings)
  Notable initiatives but very little sharing (i.e starlink/spaceX)
    Use of custom/proprietary code
    Open initiatives are emerging !
      Space Grade Linux (SGL) https://elisa.tech/space-grade-linux-sig/

## Slide 79
The end
This document is the property of CNES. It cannot be used without their consent